## Slide 1
INTERNSHIP REVIEW 1
Networking, DHCP & Automation
IIT Madras Computer Centre
P.G. Senapathy Centre for Computing Resources
NETWORK
DHCP
AUTOMATION
DNS
1 - 8 September 2026

## Slide 2
Internship Journey
From understanding operations to automating DHCP reservations
Network Troubleshooting
DHCP
DHCP Reservation
Kea DHCP
Automation
DNS
Understand network → Control DHCP → Automate reservations

## Slide 3
Real Network Troubleshooting
High CPU utilization in network devices
PROBLEM High CPU usage
•
Investigated CPU utilization and historical trends
•
Identified SISF as a significant CPU consumer
•
Studied IPv6 and Neighbor Discovery
•
Performed a controlled IPv6 test
•
Observed impact and restored configuration
Monitor
Analyze
Test
Evaluate
Rollback
Key lesson: Improve performance without affecting services.

## Slide 4
DHCP Server Implementation
Configured and validated DHCP client allocation
Linux DHCP Server
Network Switch
Laptop Client
Server → Switch → Client
•
Installed DHCP server
•
Configured subnet and IP pool
•
Configured gateway and DNS
•
Tested DHCP client allocation
•
Verified IP configuration
DHCP HANDSHAKE
Discover
Offer
Request
ACK

## Slide 5
DHCP Reservation
Same MAC address → predictable IP address
Client MAC Address 30:13:8B:C4:06:3D
Reserved IP Address 192.168.10.151
•
Identified the client MAC address
•
Created DHCP reservation
•
Renewed the client lease
•
Verified the reserved IP
Result: The same client receives a predictable IP based on its MAC address.

## Slide 6
ISC DHCP → Kea DHCP
A move from manual configuration toward API-based management
ISC DHCP
Kea DHCP
•
Manual configuration
•
File-based workflow
•
More repetitive administration
•
DHCPv4
•
Control Agent
•
REST API
•
Automation-ready
Kea enabled API-based DHCP management for automation.

## Slide 7
Kea Control Agent & API
Programmatic management path for DHCP reservations
Python Script
REST API
Kea Control Agent
Kea DHCPv4
•
Control Agent provides an interface to manage Kea
•
Python communicates with Kea through the REST API
•
Reservations can be created and verified programmatically

## Slide 8
Automated DHCP Reservation
Main workflow: spreadsheet-driven reservation management
Google Sheet
Published CSV
Python Automation
Kea Control Agent API
Kea DHCPv4
DHCP Client
Reserved IP
•
Google Sheet stores hostname, MAC and reserved IP
•
Python retrieves and validates the data
•
Python sends reservation requests through the Kea API
•
Kea creates the reservation
•
Client receives the reserved IP
AUTOMATION
Input Hostname • MAC • IP
Output Reserved IP

## Slide 9
End-to-End Testing
Validated the complete path from input data to the DHCP client
Input
Processing
API
DHCP
Client
Result
✓
CSV retrieval
✓
Python processing
✓
API communication
✓
Reservation creation
✓
Reservation verification
✓
Client receives reserved IP
Example MAC: 30:13:8B:C4:06:3D → Reserved IP: 192.168.10.151

## Slide 10
DNS Server Implementation
Configured and validated DNS resolution with a ping test
Linux DNS Server
Laptop Client
Server → Client
•
Installed DNS server
•
Configured DNS zone and records
•
Configured client to use DNS server
•
Tested resolution by pinging www.example.com
•
Verified successful reply from the server
DNS RESOLUTION & PING TEST
DNS resolver (Query)
Root name server
TLD name server
Eg: .com
Athoritative name server
ping
You → www.google.com → DNS Server → Finds IP Address → 142.250.xxx.xxx → Google Server → Website Displayed

## Slide 11
Key Learning & Conclusion
Technical skills developed during the internship
Network Troubleshooting
SKILL
DHCP Administration
SKILL
Kea DHCP
SKILL
DNS
SKILL
ISO LAYERS
SKILL
From manual DHCP configuration to automated reservation management & DNS config
Thank you